## Slide 1: STCV-Synth
David Cardona
Robert Fischer
DGMD-E14 – Final Project
Harvard Extension School
Fall 2021

## Slide 2: Agenda
Description
Demo
Architecture
Engine
Controllers
Data Analysis
Resources
Conclusions

## Slide 3: Description

## Slide 4: Description
First prototype in a series of accessible devices for creative expression
Audio engine controlled by a 9-DOF IMU and Computer Vision
STCV-Synth

## Slide 5: Description
Create artistic outlets for people with disabilities
Provide novel interactive approaches to interdisciplinary art performance and development
Purpose

## Slide 6: Demo

## Slide 7: Architecture

## Slide 8: Architecture
BLE

## Slide 9: Architecture
BLE
USB
Ribbon
HDMI

## Slide 10: Architecture
STMicroelectronics SensorTile*
Camera
Computer –or– NVIDIA Jetson Nano**
* Soldered to Cradle Board
** WiFi + BLE card, display, and speakers required
Materials

## Slide 11: Engine

## Slide 12: Engine
Audio DSP engine
Modular synthesizer component approach
Renders uncompressed audio files
Overview

## Slide 13: Engine
Oscillator
4th-Order Low-Pass Filter
ADSR Envelope Generator
Mixer
Long-Delay Effect
Reverb Effect
Components

## Slide 14: Engine
Oscillator
Signal Flow
Delay
ADSR
Filter
Mixer
Reverb
Mapped to Gain Multiplier
Stereo Output to DAC

## Slide 15: Engine
Scales defined as numeric series
BPM and subdivisions set as multipliers to control loop rate
Data-Driven Design

## Slide 16: Controllers

## Slide 17: Controllers – SensorTile
Data transmission via BLE GATT
Motion and Quaternion characteristics*
10,000Hz** notification sample rate
Overview
* Recorded Datalogs
** 10ms

## Slide 18: Controllers – SensorTile
No Data Pre-Processing
Calculation of Spherical Coordinates based on Acceleration
Calculation of Euler Angles based on relative Quaternions*
Data Processing
* Quaternions were calculated from the initial relative quaternion (), computing changes in the real value () by normalizing against the vector quaternion (i.e., imaginary components).

## Slide 19: Controllers – SensorTile
Spherical Coordinates – Motion
Radial Distance
Polar Angle
Azimuth Angle

## Slide 20: Controllers – SensorTile
Euler Angles – Quaternions
Roll
Pitch
Yaw

## Slide 21: Controllers – SensorTile
– ADSR Attack*, ADSR Amp. Multiplier, ADSR Duration*, Delay mixer channel volume
– LPF Cutoff Frequency
– Reverb Dry/Wet Balance
Mapping of Spherical Coordinates
* Inverse Proportion

## Slide 22: Controllers – OpenCV
Custom GUI
Hand recognition
Overview

## Slide 23: Controllers – OpenCV
GUI Elements
Buttons
Slider
Toggle
Menu

## Slide 24: Controllers – OpenCV
Hand Recognition
Index fingertip extraction
Conversion to 2D point
Bounding boxes around GUI elements
AABB 2D collision detection

## Slide 25: Data Analysis

## Slide 26: Data Analysis
Search correlations in the datalogs
Found and graphed correlations
High correspondence in acceleration data
Identification of non-linear trigonometric identities
Overview

## Slide 27: Data Analysis
DISCUSS HOW DATA WAS CLEANED
Cleanup

## Slide 28: Data Analysis
DISCUSS HOW DATA WAS PROCESSED
Processing

## Slide 29: Data Analysis
DISCUSS HOW DATA WAS VISUALIZED
Visualization

## Slide 30: Data Analysis
DISCUSS CONCLUSIONS FROM DATA ANALYSIS
Observations

## Slide 31: Resources

## Slide 32: Resources
AsyncIO – Asynchronous concurrent code
Threading – Thread-based parallelism
Python Libraries

## Slide 33: Resources
Bleak – BLE cross-platform connectivity
MediaPipe
Numpy
OpenCV
Pandas
Pyo – Audio DSP
Shapely – Analysis of planar geometric objects
Third-Party Libraries – Synth

## Slide 34: Resources
Jupyter Notebooks
MatPlotLib
Numpy
Pandas
Sci-Kit Learn – Machine learning and correlations
TensorFlow and Keras
Third-Party Libraries – Analysis

## Slide 35: Conclusions

## Slide 36: Conclusions
Conclusion 1
Conclusion 2
Conclusion 3

## Slide 37: Conclusions
Polyphony
Euler angles based musical gestures
Sustain mode
Multi-sensor operation
Future – Features

## Slide 38: Conclusions
Improve OpenCV execution
Decouple async queues for real-time improvements
Cross-platform GPU acceleration
Port to multi-thread compatible language
Future – Optimization

## Slide 39: Conclusions
Video synthesizer engine
Next Prototype

## Slide 40: Thanks!